## Slide 1: SSVEP manual

## Slide 2
EEGLAB
EEGLAB
  관련 링크: https://eeglab.org/
  EEGLAB 이란?
    MATLAB 기반의 오픈소스 EEG 분석 툴박스
    EEG 데이터를 전처리(preprocessing)·시각화·통계/시간-주파수 분석·ICA 기반 아티팩트 제거를 위해 주로 사용

## Slide 3
Data structure
Data
  File format: gdf
  EEG.data: channels(40) ⨯ timepoints(N)
    1~32(EEG), 33~34(mastoids)
  Device: Biosemi active two
  Stimuli param.: 14~21.8Hz, 0.5π phase diff
  Event marker: 11~50
Preproc param.
  Filter: bps(1-45Hz), notch(59 – 61Hz)
  Channel selection: O1, O2, Oz
  Epoching: 0~5 sec

## Slide 4
Preproc.
Data load
  File format: gdf → pop_biosig
Filter
  Band pass filter: 1-45Hz
  Band stop filter: 59-61Hz (notch filter)
Plot
  spectopo: frequecny domain
  eegplot: time domain
freq_band: [1 45]
freq_stop: [59 61]

## Slide 5
Preproc
Epoching
  Event marker: 11~50
  Epoching: 0~5 sec
Marker: 27
N sec
N sec
Epoch
Ch
window_size: [0 5]
Event marker: 11:50
Event timestemp
ch ⨯ time ⨯ class ⨯ trial

## Slide 6
Fourier trasnform
FFT
  Time to Frequency
Fs | sampling rate | 1024Hz
T | Timepoint bin | 1/1024
L | Singal length | Epoch size (5sec*srate)
t | timepoints | Vector(0~5sec)
f | Freq. point bin | Vector(0~512Hz)
Operating Column vector
Dividing L
freq
magnitude
Double to single sided spectrum
Double sided spectrum
Single sided spectrum

## Slide 7
Fourier trasnform
Padding
  3 sec of time series → 1/3Hz freq. bin
  High resolution ← increase length of time series
ep_data
ep_data_padding
5*srate → 15*srate

## Slide 8
Fourier trasnform
Padding
  3 sec of time series → 1/3Hz freq. bin
  High resolution ← increase length of time series
padding
origin

## Slide 9
Canonical correlation analysis
Method for SSVEP recognition
  Canonical correlation analysis(CCA)
    Linear relationship between EEG signal and reference signal
    Find highest correlation value between EEG signal and reference signal for each frequency
    In standard CCA method, sinusoidal wave was used to reference signal
SSVEP recognition based CCA method

## Slide 10
Canonical correlation analysis
Reference signal

## Slide 11
Canonical correlation analysis
Correlation Coefficient
  Signal (X) Ref(~) → [, , … , ]
  argmax([, , … , ]) →
Target freq
Index of stimuli (1 to 40)

## Slide 12
Canonical correlation analysis
Coefficient

## Slide 13
Appendix

## Slide 14
Data load function
데이터 포맷 | 확장자 | 대표 로드 함수 | 예시 코드
EEGLAB dataset | .set, .fdt | pop_loadset | EEG = pop_loadset('filename','sub01.set','filepath',rawDir);
MATLAB array | workspace variable | pop_importdata | EEG = pop_importdata('dataformat','array','data','eegdata','srate',256);
MATLAB file | .mat | pop_importdata 또는 load 후 import | EEG = pop_importdata('dataformat','matlab','data','sub01.mat','srate',256);
ASCII / TXT / CSV | .txt, .csv, .asc | pop_importdata | EEG = pop_importdata('dataformat','ascii','data','sub01.csv','srate',256);
Float binary | .f32, .float 등 | pop_importdata | EEG = pop_importdata('dataformat','float32','data','sub01.f32','srate',256);
BrainVision | .vhdr, .vmrk, .eeg | pop_loadbv | EEG = pop_loadbv(rawDir,'sub01.vhdr');
EDF / BDF / GDF | .edf, .bdf, .gdf | pop_biosig | EEG = pop_biosig('sub01.bdf');
BioSemi | .bdf | pop_biosig | EEG = pop_biosig('sub01.bdf');
FieldTrip 지원 포맷 | 다양함 | pop_fileio | EEG = pop_fileio('sub01.xxx');
EGI / NetStation MFF | .mff | pop_mffimport 또는 mff_import | EEG = pop_mffimport('sub01.mff');
XDF / LSL | .xdf | pop_loadxdf | EEG = pop_loadxdf('sub01.xdf','streamtype','EEG');
Neuroscan | .cnt | pop_loadcnt 또는 pop_biosig / pop_fileio | EEG = pop_loadcnt('sub01.cnt');
EGI simple binary | .raw | pop_readegi | EEG = pop_readegi('sub01.raw');

## Slide 15
Biosemi data specific

## Slide 16
Matlab fft
Positive and negative spectrum
Single sided spectrum